## Slide 1
Blood Glucose Prediction Model Applicable to Continuous Glucose Monitoring Systems
Master Thesis Defense
Author: Jiang Yijun
Supervisor: Prof. Shiming Zhang
Department of Electrical and Computer Engineering
The University of Hong Kong
June 2026

## Slide 2
Background
Data Processing
General Models
Transfer Learning
Meta-Transfer
Conclusion
Introduction: A CGM Prediction System for Wearable Devices
If CGM becomes widely adopted (e.g., Apple Watch), what prediction system should we design?
Key requirements for an ideal CGM prediction system:
Real-time 30-minute ahead prediction
Accurate under rapid glucose changes
Personalized to individual physiology
Data-efficient: works with minimal calibration data
Privacy-preserving: local computation
This thesis proposes a complete pipeline using only CGM sequences + age + BMI
No meal logs, no insulin doses, no exercise records needed.

## Slide 3
Challenges in CGM Data and Prediction Task
Physiological Delay
5-10 minute lag between interstitial fluid glucose and blood glucose. During rapid changes (post-meal, post-exercise), dynamic error becomes significant.
Sensor Noise & Drift
Electrochemical sensor degradation, motion artifacts, pressure-induced sensor attenuation (PISA), and electronic system noise.
Data Missing
Sensor signal loss, calibration interruption, device drop, wireless transmission failure lead to gaps in time series.
Prediction Target: 30-60 minutes ahead | Goal: From after-event monitoring to pre-event prediction
Background
Data Processing
General Models
Transfer Learning
Meta-Transfer
Conclusion

## Slide 4
Heterogeneous Dataset Fusion and Standardization
Colas Dataset (T2D)
Medtronic MiniMed iPro
NGT to prediabetes to T2D
High clinical heterogeneity
Hall Dataset (Healthy)
Dexcom G4 monitoring
"Glucotypes" concept
Healthy and sub-healthy
OhioT1DM Dataset (T1D)
12 T1D subjects
Most severe fluctuations
Insulin pump treatment
Full Spectrum: Health → Prediabetes → T2D → T1D | 174 subjects, 117,570 observations
Standardization Pipeline
1. Field alignment: {id, time, gl, age, bmi}
2. Unit conversion: All to mg/dL
3. Linear resampling: Strict 5-min intervals
4. Missing data:
• ≤15 min: Cubic spline interpolation
• >15 min: Sequence segmentation (exclude <6h)
Table 2.1 Physiological Parameters
Metric | Mean±SD | Range
Age (year) | 54.7±13.2 | 25-88
BMI (kg/m²) | 29.1±4.6 | 18-44
Avg BG (mg/dL) | 111.5±38.4 | 40-350
Background
Data Processing
General Models
Transfer Learning
Meta-Transfer
Conclusion

## Slide 5
Filtering Theory and Evaluation
Table 3.2 Comparison of Filtering Results
Index | Kalman | S-G Filter | Butterworth | Ideal
NRR (%) | -6.6±3.7 | 14.0±6.2 | 18.8±7.1 | High
SNR | 7.9±2.0 | 9.4±2.2 | 9.9±2.3 | High
PPR | 1.009±0.005 | 0.987±0.007 | 0.972±0.008 | ≈1.0
Phase Lag (min) | 1.7±2.4 | 0 | 0 | 0
Analysis & Conclusion
Kalman: Negative NRR and phase lag - not suitable for prediction input
Butterworth: Highest noise removal (18.8%) but attenuates peaks (PPR 0.972) - loses 3% per peak
S-G Filter: Best balance - moderate denoising (14.0%) with excellent peak preservation (PPR 0.987)
Conclusion: S-G selected for preserving local extrema without delay
Zero phase lag ensures strict timeline alignment; third-order polynomial fits glucose smooth curves
Background
Data Processing
General Models
Transfer Learning
Meta-Transfer
Conclusion

## Slide 6
Comprehensive Performance Comparison
Table 4.1 Nine Models Comparison (30-min horizon)
Model | MAE | RMSE | MAPE(%) | RMSPE(%) | CEG A+B(%)
ARIMA | 5.80 | 8.96 | 4.47 | 6.91 | 99.8
Linear | 5.23 | 8.53 | 4.38 | 6.83 | 99.8
KNN | 11.33 | 15.63 | 9.95 | 13.63 | 93.4
Random Forest | 6.64 | 10.28 | 5.58 | 8.23 | 99.2
XGBoost | 8.22 | 12.33 | 6.98 | 10.14 | 98.1
CNN | 5.41 | 8.70 | 4.55 | 7.08 | 99.8
RNN | 7.47 | 11.03 | 6.33 | 8.93 | 99.0
LSTM | 5.02 | 8.19 | 4.27 | 6.74 | 99.8
Transformer | 6.50 | 9.14 | 5.78 | 8.00 | 99.6
Key findings: LSTM best overall (RMSE 8.19); Transformer close (9.14) with superior architecture for transfer learning; KNN unsuitable (15.63); All except KNN achieve >99% clinical safety
Background
Data Processing
General Models
Transfer Learning
Meta-Transfer
Conclusion

## Slide 7
Clinical Safety (CEGA) and Waveform Analysis
Figure 4.10 CEG Clarke Error Grid for all 9 models
Figure 4.11 Waveform comparison on Subject 306
CEGA Results: All models except KNN achieve >99% in A+B zones. LSTM, Linear, CNN, ARIMA reach 99.8% Zone A.
Waveform Analysis (Subject 306):
• Stable period: All models similar - historical values provide sufficient info
• Rapid change: Traditional models show 5-10 min phase lag; LSTM/Transformer respond acutely
• Deep learning extracts second-order dynamics (acceleration, curvature) for trend anticipation
Background
Data Processing
General Models
Transfer Learning
Meta-Transfer
Conclusion

## Slide 8
Transfer Learning Strategy: Freeze Encoder
Strategy: Pre-train → Fine-tune
Transformer decoupled into:
• Encoder: learns general glucose dynamics (shared)
• Regression Head: maps to individual-specific levels
Freeze encoder during fine-tuning, update only head
Why? 30% data (~2-3 days) too few to update all parameters
10 hold-out subjects for verification
Figure 5.1 Data split for transfer learning on Subject 306
Two-Step Process
1. Pre-train
Train on all population data
2. Fine-tune
Freeze encoder, update head
3. Personalized Model
Ready for prediction
Background
Data Processing
General Models
Transfer Learning
Meta-Transfer
Conclusion

## Slide 9
Transfer Learning Results and Waveform Improvement
Figure 5.2 Subject 124: RMSE improved 34.08%
Figure 5.3 Subject 146: RMSE improved 30.82%
Table 5.3 Transfer Learning on 10 Subjects (RMSE)
ID | 2 | 27 | 49 | 71 | 98 | 124 | 146 | 170 | 192 | 306
Baseline | 6.42 | 4.41 | 8.40 | 4.91 | 6.51 | 4.77 | 5.59 | 5.13 | 4.47 | 13.59
Improve | +18.9% | +16.6% | +9.2% | +35.5% | +1.4% | +34.1% | +30.8% | +19.6% | +32.3% | +6.6%
Average RMSE reduction across 10 subjects: 20.35%
Background
Data Processing
General Models
Transfer Learning
Meta-Transfer
Conclusion

## Slide 10
Clinical Dilemma: Extreme Few-Shot Scenario
What if only one day data is available? 30-50 samples (~2.5 hours)
Standard transfer learning fails:
• Prediction head cannot move far enough from pre-trained weights
• Standard pre-training optimizes average loss across all subjects
• Not close to best weights for any one person
Meta-learning solution:
Instead of optimizing for average fit, optimize initialization for rapid adaptation
Find parameter point where a few gradient steps produce large error drop
FOMAML Key Difference
Standard Pre-training:
Minimize average loss: θ* = argmin ΣL(f_θ, D_i)
FOMAML:
Optimize for fast adaptation:
θ* = argmin ΣL(f_θ', D_i^query)
where θ' = θ - α∇L(f_θ, D_i^support)
Outer objective evaluates performance AFTER adaptation
First-Order approximation eliminates Hessian computation - suitable for resource-limited devices
Background
Data Processing
General Models
Transfer Learning
Meta-Transfer
Conclusion

## Slide 11
Learning Curves: Basic vs Meta Transfer
Figure 6.2 Learning curve: Basic Transfer vs Meta Transfer (Subject 124)
Key Findings
N < 100 samples:
MAE reduced by 25.67% on average
N < 40 samples:
MAE dropped by 31.58%
N > 150 samples:
Two methods converge
Value of meta-learning specifically in low-sample regime where starting point matters most
Table 6.2 N=30 Comparison
Metric | Basic | Meta
MAE | 5.94 | 5.38
RMSE | 6.49 | 6.21
Background
Data Processing
General Models
Transfer Learning
Meta-Transfer
Conclusion

## Slide 12
Few-Shot Waveform Consistency Analysis (N=30)
Figure 6.3 Prediction comparison on Subject 124 with only 30 samples (~2.5 hours)
Detailed Observations
Rapid rise (post-meal):
• Meta Transfer tracks peak accurately
• Basic Transfer shows overshoot
Change points:
• Meta Transfer responds faster
• Significantly reduced phase lag
Stable phase:
• Similar average performance
• Meta Transfer has smaller variance
Meta Transfer: lower error + more stable
Meta Transfer not only reduces average error but also reduces error fluctuation
Background
Data Processing
General Models
Transfer Learning
Meta-Transfer
Conclusion

## Slide 13
Core Scientific Contributions
1
CGM-Only Dataset
• Uses CGM sequence + age/BMI only; no meal, insulin, or exercise logs
• Fuses 174 subjects from Colas, Hall, and OhioT1DM
• Standardizes units, 5-min sampling, missing data, and S-G filtering
2
Preprocess/Model Study Pipeline
• Quantifies CGM noise and compares Kalman, S-G, and Butterworth filters
• Benchmarks 9 models under the same 30-min prediction setting
• Selects Transformer as the personalization-ready base model
3
Few-Shot Personalization(meta
learning based on transformer)
• Frozen-encoder transfer learning reduces RMSE by 20.35%
• FOMAML improves N<40 adaptation by 31.58% MAE
• Enables day-one personalization from 30-50 CGM samples
Future Engineering Value
"Cloud pre-training + local fine-tuning" architecture:
• Cloud: Train general model on population data
• Device: Download pre-trained model
• Local: Fine-tune with user's first 2.5 hours of data
• Result: Personalized predictions from day one, no data uploaded to cloud
Background
Data Processing
General Models
Transfer Learning
Meta-Transfer
Conclusion

## Slide 14
Thank You
Questions & Answers
Jiang Yijun
Department of Electrical and Computer Engineering
The University of Hong Kong
Supervisor: Prof. Shiming Zhang
June 2026